## Slide 1
Diabetes Diagnosis
(binary classification problem)
using public ECG dataset
2025 Winter Internship: Final Presentation
Feb. 05, 2025
School of Undergraduate Studies, DGIST
Intelligent Bio-OptoMechatronics Lab.
Jeong-Ho SEO, Intern Student
Main Reference
"The impact of heart rate variability for classifying diabetes based on machine learning (Hanbeen Jung, Cheol Song).“
Pan, J., & Tompkins, W. J. (1985). A Real-Time QRS Detection Algorithm. IEEE Transactions on Biomedical Engineering, BME-32(3), 230–236.

## Slide 2
Contents: Project during this internship
  I. 1st week
    A. Project Subject
    B. Search Public ECG dataset
  II. 2nd & 3rd week
    A. Selection of ECG dataset
    B. Architecture of model
    C. Python code for extracting input features
  III. 4th week
    A. NEW ECG dataset: Extracting input features
    B. Machine Learning Algorithm
  IV. Raw ECG visualization
    A. Wearable device ECG dataset
    B. 60 Male Diabetes Type 2 ECG dataset visualization

## Slide 3
A. Project Subject
I. 1st week
Diabetes Diagnosis
using public ECG dataset.
Reference
"The impact of heart rate variability for classifying diabetes based on machine learning (Hanbeen Jung, Cheol Song).“

## Slide 4
B. Search Public ECG dataset
I. 1st week
Candidate 1. MIT-BIH Arrhythmia Database
Most Popular ECG dataset
However, Non-related to diabetes. (Arrhythmia 부정맥 dataset)
=> Not used.
source: https://physionet.org/content/mitdb/1.0.0/

## Slide 5
B. Search Public ECG dataset
I. 1st week
Candidate 2. Cerebromicrovascular Disease in Elderly with Diabetes
Previous used in conference paper (reference 9)
  "The impact of heart rate variability for classifying diabetes based on machine learning (Hanbeen Jung, Cheol Song).“
However, I hope to find another dataset & merge them all
=> Keep.
source: https://physionet.org/content/cded/1.0.1/

## Slide 6
B. Search Public ECG dataset
I. 1st week
Candidate 3. Diabetes ECG-Data
ECG data are expressed as image
However, there are no description of the dataset
I cannot convert these images to available ECG dataset
=> Not used.
source: https://www.kaggle.com/datasets/ashishsarmah/diabetes-ecg-data

## Slide 7
B. Search Public ECG dataset
I. 1st week
Candidate 4. Dataset on electrocardiograph, sleep and metabolic function of male type 2 diabetes mellitus
24-hour ECG dataset with sleep/non-sleep conditions.
Collected from 60 male type 2 diabetes (T2DM) hospitalized patients
ECG dataset & RR-interval dataset
However, there are no healthy ECG dataset (Non-diabetes dataset)
=> Not used.
source: https://data.mendeley.com/datasets/9c47vwvtss/4
article: https://www.frontiersin.org/journals/physiology/articles/10.3389/fphys.2023.1157270/full
paper: https://www.sciencedirect.com/science/article/pii/S235234092300522X

## Slide 8
B. Search Public ECG dataset
I. 1st week
Candidate 5. D1NAMO ECG Glucose Data, MIT BIH Type 1 Diabetes monitoring using ECG
The open D1NAMO dataset
A multi-modal dataset for research on non-invasive type 1 diabetes management
wearable device ECG dataset (Zephyr BioHarness 3 wearable device)
measures the ECG at a rate of 250Hz and up to 54.89mV
=> Used.
source: https://www.kaggle.com/datasets/sarabhian/d1namo-ecg-glucose-data
Data description: https://www.sciencedirect.com/science/article/pii/S2352914818301059?via%3Dihub

## Slide 9
A. Selection of ECG dataset
II. 2nd & 3rd week
(Problem) The ECG data measurement devices are all different
=> Merging and using an integrated ECG dataset: contaminated dataset.
=> Select only one dataset.(below)
I searched for several ECG dataset as I hoped to merge them all
i.e, A large integrated ECG dataset
Selection
Candidate 5. D1NAMO ECG Glucose Data, MIT BIH Type 1 Diabetes monitoring using ECG
Diabetes or Healthy
Binary classification Problem

## Slide 10
A. Selection of ECG dataset
Diabetes: 9명, 1인 4-7개 ECG dataset
Healthy: 19명, 1인 4-5개 ECG dataset
Exception: 1명, 제외처리.
# of dataset is low
Not use Deep Learning Model
=> Traditional Machine Learning Model
=> Select Input features: HRV analysis
HF, LF, VLF peak & power: 6 input features
II. 2nd & 3rd week

## Slide 11
B. Architecture of model
Extracting input features
R peaks detection from (Time, ECG) dataset
RR intervals from R peaks
HRV analysis from RR intervals (using Fast Fourier-Transform, i.e, FFT)
RR intervals: Time domain
HRV analysis: Frequency domain
=> Need FFT.
Python Code design
(Result) Failed Machine Learning Code
Too much noise in Raw dataset
Used another dataset (below)
Candidate 2. Cerebromicrovascular Disease in Elderly with Diabetes
II. 2nd & 3rd week

## Slide 12
C. Python code for extracting input features
1_data.ipynb Architecture
Library & Module
II. 2nd & 3rd week

## Slide 13
C. Python code for extracting input features
1_data.ipynb Architecture
Loading: csv files to data frames
II. 2nd & 3rd week

## Slide 14
C. Python code for extracting input features
1_data.ipynb Architecture
Loading: csv files to data frames
II. 2nd & 3rd week

## Slide 15
C. Python code for extracting input features
1_data.ipynb Architecture
Loading: csv files to data frames
II. 2nd & 3rd week

## Slide 16
C. Python code for extracting input features
1_data.ipynb Architecture
II. 2nd & 3rd week
Reference
Pan, J., & Tompkins, W. J. (1985). A Real-Time QRS Detection Algorithm. IEEE Transactions on Biomedical Engineering, BME-32(3), 230–236.
Pan–Tompkins algorithm. (2024, 12월 4일). Wikipedia. https://en.wikipedia.org/wiki/Pan%E2%80%93Tompkins_algorithm
R peaks detection from (Time, ECG) dataset
modified & simplified Pan-Tompkins Algorithm

## Slide 17
C. Python code for extracting input features
1_data.ipynb Architecture
R peaks detection from (Time, ECG) dataset
modified & simplified Pan-Tompkins Algorithm
II. 2nd & 3rd week
R peaks satisfy
local maxima, sign of derivative changes + to –
average norm of derivative: enough large => derivative threshold
My Idea
find_peaks function detects peaks : P, R, T and some peak noise
use derivative threshold
Reference
Pan–Tompkins algorithm. (2024, 12월 4일). Wikipedia. https://en.wikipedia.org/wiki/Pan%E2%80%93Tompkins_algorithm

## Slide 18
C. Python code for extracting input features
1_data.ipynb Architecture
Normalization & Bandpass filter (Butterworth filter)
Emphasize QRS frequency band
Derivative Filter: derivative change + to –
R_peaks indices candidate (1)
II. 2nd & 3rd week
R peaks detection from (Time, ECG) dataset
modified & simplified Pan-Tompkins Algorithm

## Slide 19
C. Python code for extracting input features
II. 2nd & 3rd week

## Slide 20
C. Python code for extracting input features
1_data.ipynb Architecture
Moving Average Filter: derivative_threshold from Moving Average
R_peaks indices candidate (2)
find_peaks
R_peaks indices candidate (3)
Refine peaks
R_peaks indices intersection of three candidates (1), (2) and (3)
II. 2nd & 3rd week
R peaks detection from (Time, ECG) dataset
modified & simplified Pan-Tompkins Algorithm

## Slide 21
C. Python code for extracting input features
II. 2nd & 3rd week

## Slide 22
C. Python code for extracting input features
II. 2nd & 3rd week
Sampling Frequency fs = 250 (below) Data description: https://www.sciencedirect.com/science/article/pii/S2352914818301059?via%3Dihub

## Slide 23
C. Python code for extracting input features
1_data.ipynb Architecture
Visualization
II. 2nd & 3rd week

## Slide 24
C. Python code for extracting input features
1_data.ipynb Architecture
Visualization
II. 2nd & 3rd week

## Slide 25
C. Python code for extracting input features
1_data.ipynb Architecture
Visualization
II. 2nd & 3rd week
Failed to R peaks detection
RR intervals are not periodic

## Slide 26
C. Python code for extracting input features
1_data.ipynb Architecture
Visualization
II. 2nd & 3rd week

## Slide 27
C. Python code for extracting input features
1_data.ipynb Architecture
HRV analysis
II. 2nd & 3rd week

## Slide 28
C. Python code for extracting input features
1_data.ipynb Architecture
HRV analysis
II. 2nd & 3rd week

## Slide 29
C. Python code for extracting input features
1_data.ipynb Architecture
HRV analysis
II. 2nd & 3rd week

## Slide 30
C. Python code for extracting input features
1_data.ipynb Architecture
II. 2nd & 3rd week
Too much noise
Adjusting hyper-parameters,
But failed.
=> Change ECG dataset
Hyper-Parameters (Below)
bandpass filter: lowcut, highcut, order
moving average filter: window size
Etc.

## Slide 31
A. NEW ECG dataset: Extracting input features
III. 4th week
Change ECG dataset from wearable device dataset to my mentor’s dataset
Reuse previous python code & Some addition
Addition (1)
Add Header at RAW ECG dataset

## Slide 32
A. NEW ECG dataset: Extracting input features
III. 4th week
Change ECG dataset from wearable device dataset to my mentor’s dataset
Reuse previous python code & Some addition
Addition (2)
Sampling Frequency Calculation

## Slide 33
A. NEW ECG dataset: Extracting input features
III. 4th week
Change ECG dataset from wearable device dataset to my mentor’s dataset
Reuse previous python code & Some addition
Raw ECG data Visualization (mid 5 second)

## Slide 34
A. NEW ECG dataset: Extracting input features
III. 4th week
Change ECG dataset from wearable device dataset to my mentor’s dataset
Reuse previous python code & Some addition
Filtered ECG data Visualization (mid 5 second) & R peaks detection

## Slide 35
A. NEW ECG dataset: Extracting input features
III. 4th week
Change ECG dataset from wearable device dataset to my mentor’s dataset
Reuse previous python code & Some addition
Filtered ECG data Visualization (mid 5 second) & R peaks detection
Successful R peaks detection
Periodic RR intervals

## Slide 36
A. NEW ECG dataset: Extracting input features
III. 4th week
Change ECG dataset from wearable device dataset to my mentor’s dataset
Reuse previous python code & Some addition
HRV analysis

## Slide 37
A. NEW ECG dataset: Extracting input features
III. 4th week

## Slide 38
III. 4th week
A. NEW ECG dataset: Extracting input features
Change ECG dataset from wearable device dataset to my mentor’s dataset
Reuse previous python code & Some addition
HRV analysis

## Slide 39
B. Machine Learning Algorithm
III. 4th week
Library & Module

## Slide 40
B. Machine Learning Algorithm
III. 4th week
1. Loading & Merge data

## Slide 41
B. Machine Learning Algorithm
III. 4th week
2. Stratified K-Fold (Cross-Validation)

## Slide 42
B. Machine Learning Algorithm
III. 4th week
3. Logistic Regression (1)

## Slide 43
B. Machine Learning Algorithm
III. 4th week
4. SVM (2)

## Slide 44
B. Machine Learning Algorithm
III. 4th week
5. Random Forest (3)

## Slide 45
B. Machine Learning Algorithm
III. 4th week
6. Gradient Tree Boosting (4)

## Slide 46
B. Machine Learning Algorithm
III. 4th week
7. Adaboost (5)

## Slide 47
B. Machine Learning Algorithm
III. 4th week
8. Ensemble (6, Final model)

## Slide 48
B. Machine Learning Algorithm
III. 4th week
9. Evaluation: Train Accuracy, Validation Accuracy, AUC Score

## Slide 49
B. Machine Learning Algorithm
III. 4th week
9. Evaluation: Train Accuracy, Validation Accuracy, AUC Score

## Slide 50
B. Machine Learning Algorithm
III. 4th week
9. Evaluation: Train Accuracy, Validation Accuracy, AUC Score

## Slide 51
B. Machine Learning Algorithm
III. 4th week
9. Evaluation: Train Accuracy, Validation Accuracy, AUC Score

## Slide 52
B. Machine Learning Algorithm
III. 4th week
9. Evaluation: Train Accuracy, Validation Accuracy, AUC Score

## Slide 53
B. Machine Learning Algorithm
III. 4th week
9. Evaluation: Train Accuracy, Validation Accuracy, AUC Score
Train Accuracy
100%
Overfitting
Insufficient data

## Slide 54
B. Machine Learning Algorithm
III. 4th week
9. Evaluation: Train Accuracy, Validation Accuracy, AUC Score

## Slide 55
A. Wearable device ECG dataset visualization
IV. Raw ECG visualization
Candidate 5. D1NAMO ECG Glucose Data, MIT BIH Type 1 Diabetes monitoring using ECG
csv dataset file loading

## Slide 56
A. Wearable device ECG dataset visualization
IV. Raw ECG visualization
Candidate 5. D1NAMO ECG Glucose Data, MIT BIH Type 1 Diabetes monitoring using ECG
csv dataset file graph

## Slide 57
A. Wearable device ECG dataset visualization
IV. Raw ECG visualization
Candidate 5. D1NAMO ECG Glucose Data, MIT BIH Type 1 Diabetes monitoring using ECG
전체 Raw dataset graph

## Slide 58
A. Wearable device ECG dataset visualization
IV. Raw ECG visualization
Candidate 5. D1NAMO ECG Glucose Data, MIT BIH Type 1 Diabetes monitoring using ECG
mid_time: dataset의 중앙
center_time: mid_time에서 shift_time만큼 shifting한 시각
duration_seconds: center_time을 중심으로 duration_seconds만큼 dataset 사용.

## Slide 59
A. Wearable device ECG dataset visualization
IV. Raw ECG visualization
Candidate 5. D1NAMO ECG Glucose Data, MIT BIH Type 1 Diabetes monitoring using ECG
Raw ECG data visualizaton

## Slide 60
A. Wearable device ECG dataset visualization
IV. Raw ECG visualization
Candidate 5. D1NAMO ECG Glucose Data, MIT BIH Type 1 Diabetes monitoring using ECG
Mid_time 기준 5초

## Slide 61
A. Wearable device ECG dataset visualization
IV. Raw ECG visualization
Candidate 5. D1NAMO ECG Glucose Data, MIT BIH Type 1 Diabetes monitoring using ECG
Mid_time 기준 30초

## Slide 62
A. Wearable device ECG dataset visualization
IV. Raw ECG visualization
Candidate 5. D1NAMO ECG Glucose Data, MIT BIH Type 1 Diabetes monitoring using ECG
Mid_time -1500초 기준 5초

## Slide 63
A. Wearable device ECG dataset visualization
IV. Raw ECG visualization
Candidate 5. D1NAMO ECG Glucose Data, MIT BIH Type 1 Diabetes monitoring using ECG
Mid_time +1500초 기준 5초

## Slide 64
A. Wearable device ECG dataset visualization
IV. Raw ECG visualization
Candidate 5. D1NAMO ECG Glucose Data, MIT BIH Type 1 Diabetes monitoring using ECG
Mid_time -3000초 기준 5초

## Slide 65
A. Wearable device ECG dataset visualization
IV. Raw ECG visualization
Candidate 5. D1NAMO ECG Glucose Data, MIT BIH Type 1 Diabetes monitoring using ECG
Mid_time +3000초 기준 5초

## Slide 66
A. Wearable device ECG dataset visualization
IV. Raw ECG visualization
Candidate 5. D1NAMO ECG Glucose Data, MIT BIH Type 1 Diabetes monitoring using ECG
Raw ECG dataset 전체를 visualization했을 때에는 전반적으로 noise가 심하다고 판단되어 사용하지 않았는데, (below image)
사수(정한빈 박사과정) 선배님 방식대로 Raw data graph를 가시화해서 noise가 적은 부분만 crop한 후, noise가 적은 부분들만 collect해서 사용할 수 있을 것 같습니다.
다만 Raw ECG가 0~4094 범위이기 때문에 2050~2100 사이 값을 R peaks으로 인정할 수 있는지는 확인이 필요할 것 같습니다.
Raw data에서 RR interval의 예상치와 개수가 algorithm 결과와 1:10 정도
Algorithm 결과에서 RR interval의 값이 일정하지 않음

## Slide 67
B. 60 Male Diabetes Type 2 ECG dataset visualization
IV. Raw ECG visualization
Candidate 4. Dataset on electrocardiograph, sleep and metabolic function of male type 2 diabetes mellitus
mat dataset file loading

## Slide 68
B. 60 Male Diabetes Type 2 ECG dataset visualization
IV. Raw ECG visualization
Candidate 4. Dataset on electrocardiograph, sleep and metabolic function of male type 2 diabetes mellitus
mat dataset file loading

## Slide 69
B. 60 Male Diabetes Type 2 ECG dataset visualization
IV. Raw ECG visualization
Candidate 4. Dataset on electrocardiograph, sleep and metabolic function of male type 2 diabetes mellitus
mat dataset file graph

## Slide 70
B. 60 Male Diabetes Type 2 ECG dataset visualization
IV. Raw ECG visualization
Candidate 4. Dataset on electrocardiograph, sleep and metabolic function of male type 2 diabetes mellitus
전체 24H

## Slide 71
B. 60 Male Diabetes Type 2 ECG dataset visualization
IV. Raw ECG visualization
Candidate 4. Dataset on electrocardiograph, sleep and metabolic function of male type 2 diabetes mellitus

## Slide 72
B. 60 Male Diabetes Type 2 ECG dataset visualization
IV. Raw ECG visualization
Candidate 4. Dataset on electrocardiograph, sleep and metabolic function of male type 2 diabetes mellitus

## Slide 73
B. 60 Male Diabetes Type 2 ECG dataset visualization
IV. Raw ECG visualization
Candidate 4. Dataset on electrocardiograph, sleep and metabolic function of male type 2 diabetes mellitus
Mid_time 기준 3초

## Slide 74
B. 60 Male Diabetes Type 2 ECG dataset visualization
IV. Raw ECG visualization
Candidate 4. Dataset on electrocardiograph, sleep and metabolic function of male type 2 diabetes mellitus
Mid_time 기준 5초

## Slide 75
B. 60 Male Diabetes Type 2 ECG dataset visualization
IV. Raw ECG visualization
Candidate 4. Dataset on electrocardiograph, sleep and metabolic function of male type 2 diabetes mellitus
Mid_time 기준 30초

## Slide 76
B. 60 Male Diabetes Type 2 ECG dataset visualization
IV. Raw ECG visualization
Candidate 4. Dataset on electrocardiograph, sleep and metabolic function of male type 2 diabetes mellitus
Mid_time -1500초 기준 5초

## Slide 77
B. 60 Male Diabetes Type 2 ECG dataset visualization
IV. Raw ECG visualization
Candidate 4. Dataset on electrocardiograph, sleep and metabolic function of male type 2 diabetes mellitus
Mid_time +1500초 기준 5초

## Slide 78
B. 60 Male Diabetes Type 2 ECG dataset visualization
IV. Raw ECG visualization
Candidate 4. Dataset on electrocardiograph, sleep and metabolic function of male type 2 diabetes mellitus
Mid_time -3000초 기준 5초

## Slide 79
B. 60 Male Diabetes Type 2 ECG dataset visualization
IV. Raw ECG visualization
Candidate 4. Dataset on electrocardiograph, sleep and metabolic function of male type 2 diabetes mellitus
Mid_time +3000초 기준 5초

## Slide 80
IV. Raw ECG visualization
사수(정한빈 박사과정) 선배님과 상의 후 남성 diabetes patients 중 Type 2 환자들의 Raw ECG dataset이기 때문에, (gender, type)이 모두 특정되었으므로 그렇지 않은 다른 dataset과 병합할 수 없을 것이라 생각했습니다.
다만 Diabetes Diagnosis model에서 data의 개수 자체가 현저히 부족한 상황이므로, 필요하다면 합쳐서 사용하는 것이 더 괜찮을 것 같습니다.
24H 전체 dataset을 visualization했을 때 30,000을 넘어가는 ECG값은 모두 noise인 것 같아 삭제해서 사용하면 될 것 같습니다.
다만 ECG 값에서 12,000 부근이 R peaks의 값인지, 아니면 25,000 부근이 R peaks의 값인지는 확인이 필요할 것 같습니다.
이후에는 사수(정한빈 박사과정) 선배님 방식대로 Raw data graph를 가시화해서 noise가 적은 부분만 crop한 후, noise가 적은 부분들만 collect해서 사용할 수 있을 것 같습니다.
B. 60 Male Diabetes Type 2 ECG dataset visualization
Candidate 4. Dataset on electrocardiograph, sleep and metabolic function of male type 2 diabetes mellitus

## Slide 81
Thank you for your attention
  Q&A